## Slide 1
Acoustic–Vision Collaborative Monitoring of the Fairy Pitta (Pitta nympha) on PYNQ-Z2
AMD FPGA Design Contest 2026 · Autonomous Topic, Junior Group · Platform: AMD PYNQ-Z2 (Zynq-7020 XC7Z020)
Problem & Idea
The Fairy Pitta is a nationally protected bird (IUCN Vulnerable) but nearly impossible to monitor by human patrol. Our unattended edge system lets the bird call wake the camera: no cameras running empty, no endless video storage.
INMP441 MEMS mic
I2S RX core + AXI DMA in PL · 32 kHz/24-bit, zero CPU load
▼
On-board CNN
2-s mel window → 3-layer CNN · call score ≥ 0.985
▼
Trigger file
sound event unlocks the camera pipeline
▼
YOLOv8n (ncnn)
640×480 @5 fps · conf ≥ 0.52 locks the bird
▼
Presence recording
records while bird present · delayed stop
Measured Results
Metric
Value
Note
Audio event-level recall
97.4% @0.985 / 98.1% @0.5
155 human-checked events, 9 songs
Image mAP@0.5
86.7%
training-pool protocol (honest caveat reported)
False alarms on 380 negatives
0 / 380
highest score 0.0
End-to-end trigger latency
≈10.5 s
call → recording starts, on-board log
Audio inference (one window)
2.075 s
STFT/mel/conv/numpy on ARM A9
FPGA resource usage
LUT 3.15% · WNS +2.03 ns
audio overlay; 100 MHz FCLK0
conv1 HLS GEMM kernel
6.7 ms · max err 0.00184
vs float, 205,824 points, 0/20,584 over tolerance
Reusable PYNQ skill package (decoupled from this project): 6 verified tools — .hwh register probe, block-design linter, DMA self-test, Vivado report parser, golden-result comparator, pack verifier — plus 3 templates and a 19-item pitfall list. MIT open-source, fully reproducible build scripts. Team / advisor: [to be filled after AMD template].